I/
1) deep-water : 121m
reservoir : 2125m, thickness : 8m
tuff // 3m of gas + 5m of oil in Heimdal sand // water (Heimdal)

/!\ save les 2 models WITH_HC et NO_HC

II/
1) No relevant differences between Inline WITH and NO
The same for the different offsets and frequencies. We choose an offset of 15000m and a frequency of 0,5Hz because it seems to be the most interesting plot.

2) There are also no differences between the Crossline curves.
        DEPHASAGE de pi entre cross et in chelou ??

3) There are also no differences between the different resistivity or thickness of the reservoir, it’s maybe due to the small real dimensions of the reservoir and to the low resistivity of the layer (only around times more resistant).

Hesthammer criterion : 1,01 => 1% << 15% needed for a positive result. The Hesthammer criterion is negative in our case, one more thing that suggests that the well isn’t exploitable.

III/

In our case, CSEM didn’t help to localize HC-bearing deposits, we could say that it help us to know that the deposit isn’t relevant enough.
Indeed the reservoir is too small to have an influence on the measurement (8m max). As shown by the 1% Hesthammer criterion. In view of all these results, we advise not to continue the exploitation of the Gekko well.

WHAM supposes that the subsurface resistivity is 1D thus that we have infinite layers, which isn’t the case. The influence of more conductive layers is then increased. So in our situation the reservoir layer must have a bigger influence than in reality which confirms our choice not to continue the exploitation of this well.